## Slide 1
An app ”Simulator_sensor_extension” that uses the ”simulatorextensionlibrary”
should run in SID device that are listening on CAN3 & CAN4 data.
The app records the data and saves it to files
(can3data.csv, can4data.csv, gnssdata.csv).
The files can be moved to a connected USB storage by the app.
SID device
USB
Move the data files to USB storage
Workflow to record data from SID connected on simulator

## Slide 2
Launch an emulator on the development PC
Emulator
Development PC
Use a command window and the adb tool to push the data files
(from the USB storage) to the emulator like this:
>adb devices
List of devices attached
emulator-5554 device
BH90885E4D device
>adb -s emulator-5554 push -p c:\Temp\can3data.csv /data/local/tmp/can3data.csv
>adb -s emulator-5554 push -p c:\Temp\can4data.csv /data/local/tmp/can4data.csv
>adb -s emulator-5554 push -p c:\Temp\gnssdata.csv /data/local/tmp/gnssdata.csv
USB
Connect the USB storage with the
data files to the development PC
Workflow to push recorded data into emulator.
Note! The storage path on the emulator must be /data/local/tmp/

## Slide 3
simulatorextensionlibrary.
That reads simulator machine signals (CAN4) and sensor data signals (CAN3, GNSS) and publish this data through an API.
CAN bus
CAN 3
CAN 4
/data/local/tmp/can3data.csv
/data/local/tmp/can4data.csv
/data/local/tmp/gnssdata.csv
Apps will take use of the Extension libraries to get data.
The interface for the libraries will be the same. So a switch is easy.
We need two libraries because we need a special SDK when compiling towards the SID device. The SDK is not supported in a normal Android device or in an emulator.
emulatorextensionlibrary that checks if data files exists under /data/local/tmp/.
If the data files exists, it reads the data and publish the data via an easy to use API.
If the data file is missing the data get error status.
Library to be used in Emulators
Library to be used in SID devices
How to develop App for the students....